## Slide 1
Hearing Aid for Mild Hearing Loss
Presenter:
Name: Abrar Mohi Shafee
Mat. Num: 25968

## Slide 2
The Problem
1. Many people in the world suffer from hearing loss a.k.a 'Hearing Impairment'
2. Hearing loss can be of different types (e.g. mild, moderate, severe, very severe)
The Solution
1. A hearing aid
2. I wrote a program that captures low-pitched sound through the mic and amplifies it.
3. Target group is mild hearing loss (20-40dB)

## Slide 3
How This Hearing Aid Works
1. Microphone picks up the surrounding sound
2. Amplifier makes the sound louder
3. Receiver sends the amplified sound

## Slide 4
Program Explanation Page 1
Screen Configuration
screen = get(0,'ScreenSize');
P1 = [50 300 screen(3)/2 screen(4)/2];
P2 = [620 80 screen(3)/2 screen(4)/2];
Microphone Parameters
samplesPerSecond = 1024;
framesPerSecond = 44100;
t = 30;
numPlays = (t*framesPerSecond) / samplesPerSecond;
Audio Recording
mic = audioDeviceReader;
mic.SamplesPerFrame = samplesPerSecond;
mic.SampleRate = framesPerSecond;
1
2
3
4
5
6
7
8
9
10

## Slide 5
Program Explanation Page 2
Audio Playback
audioPlayer = audioDeviceWriter('SampleRate',framesPerSecond);
Scope Parameters
scope = dsp.TimeScope('SampleRate',framesPerSecond,'TimeSpan',0.1,... 'Position',P1,'YLimits',[-1 1]);
scope.ShowGrid = 1;
scope.ShowLegend = 1;
Spectrum Analyzer
graph = dsp.SpectrumAnalyzer('SampleRate',framesPerSecond,'Position',P2,... 'PlotAsTwoSidedSpectrum',false);
graph.SpectrumType = 'Spectrogram';
11
12
13
14
15
16
17
18

## Slide 6
Program Explanation Page 3
Stream Loop
while numPlays>0
data = step(mic);
step(audioPlayer, double(data));
step(scope,data);
step(graph,data);
numPlays = numPlays-1;
end
Release Hardware
release(mic);
release(audioPlayer);
release(scope);
release(graph);
19
20
21
22
23
24
25
26
27
28
29

## Slide 7
The Result
Time Scope
Spectrum Analyzer
The amplified sound is played back in real time

## Slide 8
Project source code can be found on:
https://github.com/abrarmohi/hearing-aid

## Slide 9
References
Hearing Loss - https://en.wikipedia.org/wiki/Hearing_loss
Hearing Aid Basics - https://www.webmd.com/healthy-aging/hearing-aids#1
Simple Hearing Aid - https://de.mathworks.com/matlabcentral/fileexchange/50905-simple-hearing-aid